## Slide 1
ECRIO INTERNSHIP · 2026
Wellhead Pressure
Monitoring Dashboard
A live view of tubing, casing and annulus pressure across every well — so nobody has to drive out and read a gauge to find out something's wrong.
Built during my Ecrio internship | Frontend: React.js + Tailwind CSS | Backend: Python + FastAPI
Presented by
Selvamani M

## Slide 2
THE PROBLEM
Problem Statement
Why wellhead pressure monitoring needs to change
1
Manual Monitoring
Traditional wellhead pressure monitoring requires manual gauge readings and frequent field visits, which consume time and involve safety risks.
2
Lack of Real-Time Monitoring
There is no centralized dashboard to continuously monitor tubing, casing, and annulus pressures across multiple wells.
3
Delayed Fault Detection
Abnormal pressure conditions, unexpected shut-ins, and sudden pressure changes may not be detected promptly.
4
Well Integrity Risks
Sustained casing pressure and abnormal annulus pressure buildup beyond MAASP can indicate potential well integrity problems.
5
Production Loss
Issues such as blockage, sand-up, and hydrate formation can affect well performance and reduce production.
6
Sensor Faults
Faulty, drifting, or stuck sensors can produce unreliable readings and lead to incorrect alarms.
7
Lack of Automated Alerts
Manual monitoring may delay the notification of critical pressure conditions to field operators and well-integrity engineers.
8
Need for a Centralized Solution
A real-time monitoring dashboard is required to validate sensor data, detect abnormal conditions using rule-based logic, display pressure trends, and generate severity-based alerts for faster and safer decision-making.

## Slide 3
THE SOLUTION
Problem Solution
How the Wellhead Pressure Monitoring Dashboard answers each problem
1
Centralized dashboard
Replaces manual gauge readings and field visits with one continuously live view — safer, faster, no site drives.
2
Field-wide live monitoring
A single dashboard continuously tracks tubing, casing, and annulus pressure across every well in the stock.
3
Instant fault detection
Continuous data acquisition with rule-based logic flags abnormal conditions, shut-ins, and sudden changes the moment they occur.
4
Integrity alarms against MAASP
Automatically tracks casing pressure and annulus build-up against MAASP, raising integrity alerts before they escalate.
5
Early production-loss signals
Drawdown and trend analysis surfaces blockage, sand-up, and hydrate-formation patterns before output visibly drops.
6
Sensor validation
Built-in checks distinguish faulty, drifting, or stuck sensors from genuine alarms, filtering out unreliable readings.
7
Automated, severity-based alerts
Alerts route automatically to field operators and well-integrity engineers by severity — no one has to notice first.
8
One integrated workflow
Validates sensor data, applies rule-based detection, visualizes pressure trends, and drives faster, safer decisions — end to end.

## Slide 4
System Archietecture

## Slide 5
WHY I BUILT THIS
Somebody was driving to every wellhead just to read a gauge
Manual rounds, real risk
Field operators were physically driving from well to well to check tubing, casing and annulus pressure — slow, and it puts people on-site more than it needs to.
Only a snapshot in time
Readings happened whenever someone visited. Anything that changed between visits was simply invisible until the next round.
The risky stuff is silent
Sustained casing pressure and annulus build-up against MAASP — the early warning signs of a leak — don't announce themselves. They just sit there until someone checks.
02

## Slide 6
WHAT I SET OUT TO DO
One screen.
Every well.
Every warning sign.
My goal was simple: give operations and integrity engineers one live place to watch pressure across the whole well stock, with alarms that fire on their own when something's actually wrong.
Catch leaks before they're a problem
Watch for sustained casing pressure and annulus build-up against MAASP — the earliest signal of a containment issue — instead of finding out after the fact.
Notice production loss early
Pick up on blockage, sand-up and hydrate formation through drawdown patterns, rather than waiting for output to visibly drop.
Cut out the gauge walk entirely
Replace the hazardous site-to-site visits with one dashboard anyone on the team can pull up from their desk.
03

## Slide 7
HOW THE DATA MOVES
From a sensor on the wellhead
to a reading I can trust
Tubing head, each accessible casing annulus (A / B / C), the flowline and the choke are all read every 1–10 seconds from wellhead RTUs.
01
SENSORS ON SITE
Pressure transmitters on the tubing head, casing annuli A/B/C, flowline and choke.
02
RTU PICKS IT UP
Every 1–10 seconds, readings are sampled and published from the wellhead RTU.
03
I VALIDATE IT
Range checks, drift checks, stuck-sensor checks — a bad instrument becomes its own alarm, not a false reading.
04
CLEAN, TAGGED DATA
What's left is a normalised, well-tagged reading the rule engine and dashboard can actually use.
04

## Slide 8
HOW THE ALARMS DECIDE
A YAML file per well tells the rules what "normal" looks like
Completion type, which annuli exist, MAASP per annulus, tubing MAOP, the normal operating band, expected shut-in pressure — one register per well drives every rule below.
Tubing HI/HIHI · LO/LOLO
The standard threshold alarms, checked against that well's own operating band.
Annulus over MAASP
Any accessible annulus — A, B or C — crossing its Maximum Allowable Annulus Surface Pressure.
Casing pressure that won't bleed down
This is the one I care about most — it's the clearest early sign of a containment problem.
Fast pressure swings (dP/dt)
A sudden rate-of-change spike that usually means a leak or a slug moving through.
Build-up rate after bleed-down
Compares what happens right after a bleed-down against what's actually acceptable for that well.
Ignoring alarms I caused myself
If an operator changes the choke on purpose, the resulting alarm gets suppressed instead of paging someone for nothing.
05

## Slide 9
HOW IT'S BUILT
A pretty lean, real-time web stack
Wellhead RTUs
1–10s sensor reads
FastAPI backend
Ingestion · validation · rule engine
Well register (YAML)
MAASP · MAOP · bands
React + Tailwind UI
Live dashboard · alarms
Frontend — React.js + Tailwind CSS
The colour-coded well tiles, the drill-down trend views, the integrity watch-list — all built as fast, reusable components so adding a new panel doesn't mean starting over.
Backend — Python + FastAPI
Handles ingestion from the RTUs, runs the validation and the YAML-driven rule engine, classifies well-state changes, and routes alarms by severity.
06

## Slide 10
WHAT IT LOOKS LIKE TO USE
What ops and integrity actually see
Colour-coded well tiles
The whole field at a glance — tile colour follows the live alarm state, nothing to dig for.
Drill-down trend views
Click a well and you're straight into its tubing, casing and annulus history.
Integrity watch-list
Wells with active or building MAASP / bleed-down risk, sorted by how urgent they are.
WHO GETS PAGED, AND WHEN
WARNING
Field operator
Early-stage stuff — operating-band excursions, minor drift. Worth a look, not a scramble.
CRITICAL — INTEGRITY
Well-integrity engineer
MAASP breach, sustained casing pressure, a bleed-down that didn't work.
CRITICAL — HSE
HSE team
Anything that looks like a containment risk — this one can't wait.
07

## Slide 11
WHAT'S ACTUALLY RUNNING
Here it is, running in Docker
This isn't a mockup — it's a screenshot off my own machine, tracking the full well stock Dashboard.
10 active wells
Full field overview, one tile per well.
3 warnings, 3 critical
Clean at the moment I took this — the thresholds come straight from the YAML register.
Live sensor feed
Tubing, Annulus A/B, flowline and choke, updating per well.
08

## Slide 12
Wells

## Slide 13
Alarm Center

## Slide 14
Integrity Watchlist

## Slide 15
Production

## Slide 16
WHAT CHANGES
From driving out to just... checking a screen
24 / 7
Continuous automated watching, instead of periodic manual reads
1–10s
How often each sensor tag refreshes across the well stock
3
Pressure zones tracked per well — tubing, casing, annulus A/B/C
0
Site drives needed just to check a pressure gauge
Warnings go to the field operator, integrity alarms go to the integrity engineer, and anything HSE-level goes straight to the safety team — automatically, based on severity, not on who happens to notice first.
09

## Slide 17
Thanks for listening
Happy to answer questions on any part of the build.
Ecrio Internship | React.js + Tailwind CSS | Python + FastAPI